## Slide 1: Information model for the rib
Nitin Bahadur, Ron folkes @ juniper
Sriganesh kini @ ericsson
Jan medved @ cisco
IETF 87, I2RS WG

## Slide 2: Information model for the rib
Nitin Bahadur, Ron folkes @ juniper
Sriganesh kini @ ericsson
Jan medved @ cisco
IETF 87, I2RS WG

## Slide 3: background
Number of i2rs use-cases require programmatic control to the routing sub-system. This draft addresses this requirement.
Not restricted to network devices. Servers and hosts can also implement the same model.
Types of operations needed:
    Read
    Write
    Events & Notifications
  Draft is an INFO model and not a DATA model. For differences, please see RFC3444.
    We do have a rough data-model if you are interested

## Slide 4: Read data – what gets read FROM the rib
Routes and their associated next-hops
RIB and other higher level abstractions that allow one to make sense of the routes

## Slide 5: Write data – what gets written into the rib
No direct programming of the FIB
Routes are programmed into the RIB
  Unicast
  Multicast
  MPLS
Route points to next-hops
RIB manager MAY do next-hop resolution
  E.g. Next-hop specified by i2RS may specify egress point, but not the transport to reach that point

## Slide 6: What happens when routes are programmed?
Each route programming results in a response containing:
  Installed – Yes/No (route got installed in FIB?)
  Active – Yes/No (route is fully resolved and is a candidate for selection?)
  Reason (E.g. Not authorized)

## Slide 7: Async notifications
Async notifications are sent by i2RS agent to Controller on a RIB change
  Route change notification (route installed?)
  Route resolution status (resolved/unresolved?)
  Reason for notification
RIB change event examples
  Active route is no longer active because of a better admin-distance route by protocol FOO
  Inactive route became active as a side-effect of transport LSP coming UP

## Slide 8: Modeling a basic routing instance
Removed RIB as an encapsulating object for routing instance
IETF community needs to decide on name for encapsulating routing-instance object for I2RS overall
routing-instance
interface (list)
RIB (list)
0..N
1..N
route (list)
0..N

## Slide 9: Modeling a route
route
route-attributes
match
0..N
0..N
nexthop-list
ipv4-route
ipv6-route
mpls-route
mac-route
interface-route

## Slide 10: Modeling a nexthop
nexthop-list
nexthop-list-member
special-nexthop
1..N
nexthop-chain
1..N
nexthop
1..N
nexthop-id
egress-interface
Logical tunnel
tunnel encap
nexthop-attributes

## Slide 11: Devil is in the details
Draft tries to address complex ways of programming the RIB
Why?
  Simplistic use-case is a lab experiment, not a deployment
  Router vendors have enough experience with multiple deployments, so RIB usage is typically known

## Slide 12: Solving use-cases
Preventing DDOS attacks by installing better preferred routes
Dynamically creating replication lists (for multicast)…based of offline receiver information
Optimizing end-to-end load-balancing of traffic across multiple edge devices

## Slide 13
Lots of good feedback on the list
Resolve terminology and address review comments
Resubmit draft and re-issue call for WG adoption